Jordan University of Science and Technology

Abstract:

Authors:

A simple, rapid and selective RP-HPLC method was developed and validated for the determination of ketorolac and five piperazinylalkyl ester prodrugs. A binary isocratic mobile phase composed of a mixture of 65:35 (v/v) 0.02 M phosphate buffer (pH 5.4) and acetonitrile was used on a C18 column (125 ? 4 mm, 5 ?m). The injection volume was 25 ?L and the detection wavelength was 314 nm and the flow rate was 1.5 mL min?1. The method exhibited excellent linearity with R 2 of no less than 0.999 and intra-assay and inter-assay precision that were less than the maximum amount allowed according to Horwitz equation. The accuracy was found to be within the allowed ?15%. The limits of detection for the analytes were between 0.060 and 0.220 ?g mL?1 and the limits of quantification were between 0.183 and 0.667 ?g mL?1. This method was used successfully for the study of the solubility, stability and partition coefficients of piperazinylalkyl ester prodrugs of ketorolac.

Simultaneous RP-LC Determination of Ketorolac and its Piperazinylalkyl Ester Prodrugs