Jordan University of Science and Technology

Abstract:

Authors:

This work analyzed rarefied plume impingement on a flat plate with an arbitrary angle. For this problem, due to the rarefication effects we must use non-traditional analysis methods. A rarefied jet gas flows out of two-dimensional nozzle and impinging on a flat plate was investigated with a gaskinetic method. With a relation between velocity-directions and geometry-positions the corresponding sets of analytical solutions for the density, slip velocity, temperature, pressure, shear stress and heat flux on locations very close or right on the flat plate were obtained. Numerical simulation results obtained with the direct simulation Monte Carlo Method (DSMC) validate these analytical solutions. In general, the comparisons between the complex exact analytical solutions and the numerical results are virtually identical.

kHALEEL aL kHASAWNEH, DUAA KHAROUF

ANALYTICAL STUDY OF NON-CONTINUUM FLOW IMPINGEMENT ONTO A FLAT PLATE WITH AN ARBITRARY ANGLE